Friction Lab

Objective - During this investigation you will study the effect of certain surface conditions on the force of friction.

Procedure -

- Zero the spring scale

- Open both paper clips forming two sets of hooks.

- Attach one hook to each end of a one foot piece of string.

- Utilizing two students on the opposite ends of a narrow table, have one student hold the scale which is attached with a paper clip hook to one end of the string. Have a second student stand on the opposite side of the table and hold the surface board with the four surfaces running parallel to the string and scale.

- Place the block of wood (2 hooks) on the paper portion of the board at the edge closest to the student holding the surface board.

- Attach the string to the block using the paper clip hook.

- The student at the board end should begin easing the board towards him/herself, simultaneously indicating to the other student to note the reading from the scale.

- Average three readings on the spring scale for each trial.

- Use the following configurations for each surface (paper, cork, rubber, sandpaper).

  - Wood block alone

  - Woodblock + one weight.

  - Wood block + two weights.

  - Wood block + 2nd block in tandem (hook together).

  - Wood block + 2nd block on top

  - Wood block with one weight + 2nd block in tandem with one weight.

  - Wood block w/ 2 weights + 2nd block in tandem w/2 weights.

Data

Collect the following data:

| Trial | Total Mass Pulled | Weight (Normal Force) |
| --- | --- | --- |
| A |  |  |
| B |  |  |
| C |  |  |
| D & E |  |  |
| F |  |  |
| G |  |  |

| Trial | Paper – Spring Scale Reading | Cork – Spring Scale Reading | Rubber – Spring Scale Reading | Sandpaper – Spring Scale Reading |
| --- | --- | --- | --- | --- |
| A |  |  |  |  |
| B |  |  |  |  |
| C |  |  |  |  |
| D |  |  |  |  |
| E |  |  |  |  |
| F |  |  |  |  |
| G |  |  |  |  |

Results

            - Plot Spring Scale Force (N) (y-axis) vs. Weight (Normal Force) (N) x-axis

            - Given the formula: F=μN. Calculate the coefficient of friction (μ) for each surface using graph ( Hint calculate the slope of the line.)

            - What effect does the variable of surface area have on frictional force?